## Slide 1: Addition Polymer Part II
Jimmy Ip 13
Andy kwok 14
Kim leong 18
Dicky ng 23
Vincent si 25

## Slide 2: Content
Polyethene
  High and low density
Polypropene
Polyvinyl choride
Polystyrene
  Expanded polystyrene
Perspex

## Slide 3: Polyethene
Addition polymer of ethene
Low-density polyethene (LDPE)
High-density polyethene (HDPE)
Very cheap

## Slide 4: Low-density polyethene
Melting point: 105℃
Softens in boiling water
Flexible

## Slide 5: High-density polyethene
Melting point: 135℃
Rigid

## Slide 6: Polypropene

## Slide 7: Polypropene
Melting point: 165℃
↓ between low and high density
Resists to…
Chemical solvents , acid, alkalis

## Slide 8: Example
Ropes
Fibres
Basket
Boxes
Luggage cases
Food containers
Packaging Film

## Slide 9: Polyvinyl Chloride (PVC)
Stiff and brittle
Mixed with PLASTICIZER
Become more flexible
Properties varies with the amount
X plasticizer→ quite rigid
Floor tiles
Pipes

## Slide 10: Polyvinyl Chloride (PVC)
With suitably plasticized……
Soft and flexible
Water resistant
Good insulator of electricity
X food container→ poisonous

## Slide 11: Example……
Shower curtains
Tablecloths
Raincoats
Artificial leather
Insulating coverings for wires

## Slide 12: Polystyrene(PS)
Transparent, hard
Brittle

## Slide 13: Polystyrene(PS)
Example:
cups, compact disc cases, measuring cups

## Slide 14: Expanded Polystyrene
Heating granular polystyrene(with a foaming agent) → Expanded Polystyrene
White solid foam
Very low density
Pretty rigid
Excellent heat insulator and shock-absorbent
Non-toxic

## Slide 15: Expanded Polystyrene
Example:
disposable cups and food boxes
lightweight ceiling tiles

## Slide 16: Perspex
Or called polymethyl methacrylate/ acrylic
Hard, tough, rigid
Highly transparent
But easily scratched
Substitute for glass

## Slide 18: Perspex
Example:
Aeroplane windows
Advertising sign boxes
Plastic optical fibres
Illuminated signs